## Slide 1
SWIP” 5st Team 4
2023. 03. 27 (Day 3)
Youngchan Jung , Chae Jongyoon , Junho Hwang , Hyelin Jung
Rear Parking Collision-Avoidance
Assist System
“후방주차 충돌방지 시스템＂

## Slide 2
Contents
Introduction | 
H/W & S/W Configuration | 
Demo Scenarios Conclusion | 

## Slide 3
Junho Hwan
Hyelin Jung
Introduction
Team Members (* means team leader)
Jongyoon Chae
Youngchan Jung
Team Leading Writing Docs
Control Section
Detection Section
Control Section Writing Docs
Control Section Detection Section Writing Docs
Detection Section Writing Docs

## Slide 4
Introduction
Rear Parking Collision-Avoidance Assist System
Rear parking assistance system using ultrasonic sensors
ADVANTAGES
Prevent pedal misoperation
Prevention of personnel accidents
Reduced driver fatigue

## Slide 5
~10cm : Red light ON & Beep
10~20cm : Blue light ON & Beep
20~30cm : Blue light ON
  Obstacle detection & Warning Signal according to distance
    30 cm ~ : Obstacle detection x
    20~30 cm : Obstacle detection(Blue) & No Warning Signal
    10~20 cm : Obstacle detection(Green) & Weak Warning Signal(Low Tone & Frequency)
    ~ 10 cm : Obstacle detection(Red) & Strong Warning Signal(High Tone & Frequency)
Introduction

## Slide 6
Hardware Configuration
H/W & SW Configuration
[ Hardware Configuration ]

## Slide 7
[ Hardware Configuration ]
⑥
① Digital MCU
② Ultrasonic
: Object detection
③ Red/Blue LED
: Gear Status
④ RGB LED
: Object Detection
Status
⑤ Buzzer
: Warning Alarm
⑥ Potentiometer
: Gear Input
④
⑤
③
②
①
H/W & SW Configuration

## Slide 8
Ultrasonic Sensor : Object Detection
: Triggered every 1msec for object detection / Echo signal is returned to the Digital MCU → Distance calculation.
H/W & SW Configuration

## Slide 9
Potentiometer : Gear Input
: Rotating the potentiometer allows to select the gear. → 3 Status : Off / Drive (D) / Reverse (R)
H/W & SW Configuration

## Slide 10
Red/Blue LED : Gear Status
: Informs the status of the gear → Red : Drive / Blue : Reverse
H/W & SW Configuration

## Slide 11
RGB LED : Object Detection Status
: Based on the distance, RGB LED shows the object detection status with 3 different color ( R / G / B )
H/W & SW Configuration

## Slide 12
Buzzer : Warning Alarm
: As the distance gets closer buzzer informs a warning signal. → Frequency of warning signal increases.
H/W & SW Configuration

## Slide 13
② Drive Mode
① Parking Mode
③ Reverse Mode
Operation Flow Chart
[ Operation flow chart ]
H/W & SW Configuration

## Slide 14
  Demo Scenarios
Demo scenario 1.
Gear : P / N
All LEDs are off and no buzzer sounds.
[ Demo Scenario 1 ]

## Slide 15
Demo scenario 2.
Gear : D
The blue LED next to the gear turns on and no buzzer sounds.
[ Demo Scenario 2 ]
  Demo Scenarios

## Slide 16
Demo scenario 3.
Gear : R
Distance from an obstacle > 30 cm
The red LED next to the gear turns on and no buzzer sounds.
Obstacle
D > 30cm
[ Demo Scenario 3 ]
  Demo Scenarios

## Slide 17
Demo scenario 4.
Gear : R
30 cm > Distance from an obstacle > 20 cm
The blue LED on the left side of the HUD turns on and no buzzer sounds.
Obstacle
20 cm < D < 30cm
Still on
[ Demo Scenario 4 ]
  Demo Scenarios

## Slide 18
Demo scenario 5.
Gear : R
20 cm > Distance from an obstacle > 10 cm
The green LED on the left side of the HUD turns on and there is weak warning sounds.
Obstacle
10 cm < D < 20cm
Still on
Low tone warning sounds
[ Demo Scenario 5 ]
  Demo Scenarios

## Slide 19
Demo scenario 6.
Gear : R
Distance from an obstacle < 10 cm
The red LED on the left side of the HUD turns on and there is strong warning sounds.
Obstacle
20 cm < D < 30cm
Still on
High tone warning sounds
[ Demo Scenario 6 ]
  Demo Scenarios

## Slide 20
Works | Team | Time (hour) |  |  |  |  |  |  |  |  | ETC
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 
Decision | Topic Selection : Rear Parking Collision-Avoidance Assist System |  |  |  |  |  |  |  |  |  | -
 | Device Selection |  |  |  |  |  |  |  |  |  | -
 | Performance Evaluation |  |  |  |  |  |  |  |  |  | -
Detection & Control | Coding for ultrasonic sensor |  |  |  |  |  |  |  |  |  | -
 | Coding for Led & RGB Led |  |  |  |  |  |  |  |  |  | -
 | Coding for Buzzer |  |  |  |  |  |  |  |  |  | -
Day1
Day2
Day3
  Conclusion

## Slide 21
Thank you